## Slide 1
Maine Water Temperature Working Group Meeting
Augusta, ME
December 3, 2019
Applications of a high-resolution version of the New England spatial statistical network model to
the Meduxnekeag: Restoration potential for thermal regimes
Naomi Detenbeck (U.S. EPA ORD)
Stephanie Figary (former ORISE at ACESD)
Cara O’Donnell (Houlton Band of Maliseets)
Office of Research and Development
Center for Environmental Measurement and Modeling/Atlantic Coastal Environmental Sciences Division Division
12/03/2019

## Slide 2: Goals
Overall: Expand habitat for brook trout and restored native Atlantic salmon populations
Determine location of existing cold water refuges for salmonids and brook trout
Select areas for riparian restoration

## Slide 3: Spatial Statistical Network Models
Linear regression models
Built on stream/river network (e.g., NHDPlus)
Account for spatial autocorrelation (tendency for points close together to be more similar)
  If spatial autocorrelation is ignored, this increases the probability of Type I errors – assuming effects are significant when they aren’t
  Use watershed area (indicator of discharge) as a weighting factor for relative influence

## Slide 4: Spatial Statistical Network Models
Linear regression models
Built on stream/river network (e.g., NHDPlus)
Account for spatial autocorrelation (tendency for points close together to be more similar)
  If spatial autocorrelation is ignored, this increases the probability of Type I errors – assuming effects are significant when they aren’t
  Use watershed area (indicator of discharge) as a weighting factor for relative influence
SSN model: quick review

## Slide 5: Spatial Statistical Network Models
Linear regression models
Built on stream/river network (e.g., NHDPlus)
Account for spatial autocorrelation (tendency for points close together to be more similar)
  If spatial autocorrelation is ignored, this increases the probability of Type I errors – assuming effects are significant when they aren’t
  Use watershed area (indicator of discharge) as a weighting factor for relative influence
SSN model: quick review
Stream network

## Slide 6: Spatial Statistical Network Models
Linear regression models
Built on stream/river network (e.g., NHDPlus)
Account for spatial autocorrelation (tendency for points close together to be more similar)
  If spatial autocorrelation is ignored, this increases the probability of Type I errors – assuming effects are significant when they aren’t
  Use watershed area (indicator of discharge) as a weighting factor for relative influence
SSN model: quick review
Stream network
Euclidean
Tail-Up (flow connected)
Tail-Down (flow
unconnected)

## Slide 7: SSN predictors of New England median July/August stream/river temperature
Shaded solar radiation
  Topographic shading
  Riparian shading
Median air temperature
Urban heat index
Percent coarse surficial deposits*
Main channel slope
Watershed storage (lakes + wetlands)
Upstream lake presence & depth
Energy inputs
Groundwater inputs
Retention time
* August only
6

## Slide 8: New England SSN model Riparian restoration scenario
2006 land cover
Canopy cover Watershed storage
Average 2002-2010 median July air temperature
Beachene et al. (2014) thermal regime classes
Tidal class assigned based on maximum elevation of reach < 3 meters
Watersheds extending into Canada not included
(1:100K)
->100%

## Slide 9: New England SSN model Riparian restoration scenario
2006 land cover
Canopy cover Watershed storage
Average 2002-2010 median July air temperature
Beachene et al. (2014) thermal regime classes
Tidal class assigned based on maximum elevation of reach < 3 meters
Watersheds extending into Canada not included
(1:100K)
->100%

## Slide 10: New England SSN model Riparian restoration scenario
2006 land cover
Canopy cover Watershed storage
Average 2002-2010 median July air temperature
Beachene et al. (2014) thermal regime classes
Tidal class assigned based on maximum elevation of reach < 3 meters
Watersheds extending into Canada not included
(1:100K)
->100%

## Slide 11: Background: Meduxnekeag Watershed
1336 km2 watershed
Flows through the Houlton Band of Maliseet Indian’s Tribal Land
HBMI goals:
Project:
  1: Determine the locations of existing cold water refuges
  2: Select areas for riparian restoration
Overall: Expanding habitat for Brook Trout and restoring native Atlantic Salmon populations
Maine
New Brunswick
New Brunswick
Maine
St. John River

## Slide 12: Scientific Objectives
Develop fine-resolution (1:24K) stream temperature prediction model for Meduxnekeag subwatershed
  Spatial resolution appropriate for examining riparian buffer management scenarios
  Address challenge of combining data sources across international boundary
Apply new method to fill in monitoring gaps (spatial coverage and key attribute ranges)
Evaluate alternative predictor variables (e.g. riparian buffer width, buffer distance upstream)
Predict thermal regime distribution across watershed
  Monthly variation
  Growing season maximum
  Wet versus dry year comparison
  Current conditions vs restored riparian zone condition
    Wet year
    Dry year

## Slide 13: Monitoring stations
37 existing temperature stations (2009 - 2018)
Added stations in 2018:
Characterized site upstream drainage areas and watershed catchments (NHDplus V2):
  Drainage area
  Slope
  Baseflow
  Discharge
  % Forested stream buffer
  % Impervious cover
  Elevation
Used principal component analysis to suggest areas for additional monitoring in 2018
12 new sites

## Slide 14: Principal Components Analysis to find major axes of variation in subcatchments
 | Eigenvectors |  | 
Original variable | PC1 | PC2 | PC3
Drainage area | -.28 | .31 | -.39
Slope | .28 | -.19 | .29
July discharge/watershed area | .35 | -.24 | .27
Aug discharge/watershed area | .39 | -.12 | .18
Catchment % forested | .31 | .10 | -.28
Catchment buffer % forested | .28 | .18 | -.43
Catchment % impervious | -.31 | -.20 | .24
Catchment buffer % impervious | -.38 | -.19 | .16
Elevation | .38 | -.03 | -.15
Catchment baseflow index | .02 | .60 | .36
Watershed baseflow index | .10 | .56 | .41

## Slide 15: Model development: Parameters
New England model as guidance:
  Air temperature
    Monthly and annual
  Imperviousness or Urban heat island
  Watershed area
  Local channel gradient or main channel slope, squared, cubed
  Extremely well drained soils or coarse surficial deposits
  Drainage density
  Lake and wetland storage
  Discharge
  Width to depth ratio
  Lake upstream
    Lake depth
  Shaded solar radiation

## Slide 16: Model development: Parameters
New England model as guidance:
  Air temperature
    Monthly and annual
  Imperviousness or Urban heat island
  Watershed area
  Local channel gradient or main channel slope, squared, cubed
  Extremely well drained soils or coarse surficial deposits
  Drainage density
  Lake and wetland storage
  Discharge
  Width to depth ratio
  Lake upstream
    Lake depth
  Shaded solar radiation
Meduxnekeag adjustments al
  % development
  Baseflow recession coefficent
  Upstream depth
  + % site in USA

## Slide 17: Model fitting for each month
Started with the parameters in the NE model
Longitude
Latitude
Velocity
Elevation
Drainage Density
% wetlands and lakes
Monthly air temp
Annual air temp
% watershed in USA
Monthly reference flow
Baseflow recession coefficient
Stream Width:Depth
% development in last 500m of basin
Main channel slope
Maximum near-upstream depth
Shaded- solar radiation
Backwards step-wise regression
Longitude
Drainage Density
% wetlands and lakes
Monthly air temp
% watershed in USA
Monthly reference flow
Baseflow recession coefficient
% development in last 500m of basin
Main channel slope
Maximum near-upstream depth
Shaded- solar radiation
Examples:
Site in Canada
% dev in 1 km/ whole watershed
Local gradient
Shaded-solar radiations (39)
Substitute parameters (11)
Add in interaction terms
Squared main channel slope
Width:depth * monthly air
Select spatial autocorrelation model

## Slide 18: Defining upstream riparian buffers
Distance upstream (as the fish swims)
Travel time upstream (as the water flows)
1 km
2 km
1 hr
2 hr
1km, 2km, 3km,4km,5km,10km,
full watershed
1hr, 2hr, 3hr, 4hr, 5hr, 6hr,12hr, 24hr

## Slide 19: Monthly and growing season models
July | August | September | Grow season max
 |  | Longitude | 
 |  | Latitude | Latitude
Soil conductivity |  |  | Soil conductivity
Gradient |  |  | Gradient
 | Channel slope2 | Channel slope2 | Channel slope2
Mx upstr depth |  | Mx upstr depth | 
Depth |  | Depth | Depth
 | Width |  | 
 |  | Wshd storage | 
 | Elevation |  | Elevation
 | Canadian | Canadian | 
Month air temp | Month air temp | Month air temp | Mx GS air temp
Month ref flow | Month ref flow | Month ref flow | GS avg ref flow
 | Month ref flow2 |  | 
3-h ups shaded solar | 3-h ups shaded solar | 3-h ups shaded solar | 1km ups shaded solar
Constant variables
Time-vary
Decrease temp
Increase temp
Bold: p < 0.05
*
*
*

## Slide 20: Monthly and growing season models (cont’d)
July | August | September | Grow season max
 |  |  | Air temp x WtoD
 |  |  | SoilCond x Main channel slope
Ref flow x airtemp |  |  | 
Spatial autocorrelation term |  |  | 
LinearSill tailup | Epanech tailup | LinearSill tailup | LinearSill tailup
Gaussian Euclidean | Gaussian Euclidean |  | 
Generalized r2 |  |  | 
0.96 | 0.89 | 0.91 | 0.88
Root mean square prediction error (deg C) |  |  | 
0.52 | 0.94 | 0.86 | 1.18
Interactions

## Slide 21: Standardized regression coefficients
 | July | August | Sept | GS max
Depth | 1.01*** |  | 1.85*** | 3.25***
Width |  | 3.26*** |  | 
Elevation |  | 1.58* |  | 2.57***
Monthly or growing season avg ref flow | -1.72*** | -2.21*** | -1.34*** | -1.58**
Monthly or max growing season air temp | 1.78*** | 2.30*** | 2.22*** | 1.56**
Canadian |  | -1.64* | -1.83*** | 
Shaded solar (3-h monthly, 1-km gs) | 0.98*** | 1.21** | 0.47 | 1.27*
Gradient | -0.60* |  |  | -0.96(*)
Longitude |  |  | 0.95 | 
Baseflow recession coefficient | -0.98** |  |  | 0.94
Channel slope2 |  | -0.58*** | -0.17 | 0.69
Latitude |  |  | -1.00** | -0.53
Mx upstream depth | 1.21*** |  | 1.16** | 
Watershed storage |  |  | -0.61 | 
Opportunities for moderating thermal regime

## Slide 22: Issues
Is apparent depth effect real?
  Both width and depth are empirical estimates based on drainage area and may be difficult to separate
  Morphometry in Meduxnekeag constrained by valley walls, low depth to bedrock
  Addition of actual channel morphometry measurements in future could improve model
Is elevation effect real?
  Elevation effects related to air temperature should have been accounted for by Daymet equations
  Comparison of Daymet with air temperatures from NE geographically weighted regressions show differences in estimated adiabatic effect
  Elevation coefficients could represent a bias correction effect for air temperature at higher elevations

## Slide 23: Effect of interannual variation in weather and month on thermal regime

## Slide 24
Thermal regime | Range
Cold water | < 19 °C
Cool water | 19 – 22.5°C
Warm water | 22.5 – 27.0°C
No survival | > 27.0°C
- - - flagged
Indicates lower confidence in results because some predictor variables are < 90% of minimum value or > 10% greater than maximum value in observation data set

## Slide 25
Dry
Wet
July thermal regime distribution
24

## Slide 26
July thermal regime distribution
Dry year – current conditions
25

## Slide 27
Dry year – Restore 30m forested buffer
July thermal regime distribution
26

## Slide 28
Dry year – Restore 90m forested buffer
July thermal regime distribution
27

## Slide 29: Percentage of reaches by thermal regime
 |  | July 2010 | - dry | July 2011 - wet |  | 
 | current | restore 30 m | restore 90 m | current | restore 30 m | restore 90 m
cold | 27.8 | 45.3 | 51.7 | 67.7 | 76.7 | 79.3
cool | 57.1 | 42.7 | 40.1 | 28.1 | 21.3 | 19.5
warm | 14.6 | 11.6 | 7.8 | 4.0 | 1.9 | 1.2
beyond survival | 0.5 | 0.5 | 0.4 | 0.2 | 0.1 | 0.1
Cold water regime expands in wet year
Effect of restoration greater in dry year
Most restoration effect associated with first 30m

## Slide 30
Growing season maximum thermal regime
Wet year – current conditions
Critical coldwater refuge areas in headwaters

## Slide 31
Growing season maximum thermal regime
Restored 30m width buffer
Critical coldwater refuge areas in headwaters

## Slide 32
Base flow Aug 1999 – dry yr
Base flow Aug 2006 – wet yr
Aug base-flow
min 3-in-5 yr trend
New England spatial statistical flow metric models
*
* Indicator of brook trout population persistence

## Slide 33: Conclusions
Potential for improved high accuracy stream temperature models, even crossing international boundaries
Potential for restoring thermal regimes through improvement of stream shading, flow regimes, stream morphometry
  Most influence in first 30m width buffers
  Buffer influence downstream: 3-hour travel time or 1 km
Critical current and future cold water refuge areas identified

## Slide 34: Questions?
Naomi Detenbeck (detenbeck.naomi@epa.gov)
Stephanie Figary (sef92@cornell.edu)
Cara O’Donnell (water@maliseets.com)

## Slide 35: Supplemental

## Slide 36: Challenge: International Boundaries
Air temperature matrix (2009-2018): DAYMET
Elevation, flowlines, discharge, velocity, lakes: NHDPlus High Resolution
Stream width and depth: Bent 2006
Canopy cover: Hansen Global Forest Change
Baseflow: Global streamflow characteristics
Lake depth: NHDPlus V2 or R package “lakemorpho”

## Slide 37: Challenge: International Boundaries
?

## Slide 38: Challenge: International Boundaries
Land use:
  US: National Land Cover Dataset
  Canada: Land Use dataset
Existing vegetation height
  US: LandFire
  Canada: Some digital surface modeling, some extrapolation
Reference flow conditions
  US: Miller et al 2018
  Canada: extrapolation of Miller et al 2018 and Bent 2006

## Slide 39: Challenge: International Boundaries
Land use:
  US: National Land Cover Dataset
  Canada: Land Use dataset
Existing vegetation height
  US: LandFire
  Canada: Some digital surface modeling, some extrapolation
Reference flow conditions
  US: Miller et al 2018
  Canada: extrapolation of Miller et al 2018 and Bent 2006

## Slide 40: Challenge: International Boundaries
Soils:
  US: SSURGO
  Canada: National soils database
Wetlands
  US: National Wetlands Inventory
  Canada: New Brunswick wetlands
Added parameters for:
  % watershed in USA
  Dummy variable
?
Rubbersheeting
?

## Slide 41: Challenge: International Boundaries
Soils:
  US: SSURGO
  Canada: National soils database
Wetlands
  US: National Wetlands Inventory
  Canada: New Brunswick wetlands
Added parameters for:
  % watershed in USA
  Dummy variable
?
Rubbersheeting
?