## Slide 1: Assessing Transportation Vulnerability and Ecological Disruption of Road-stream Crossings in the Deerfield River Watershed
Scott Jackson
UMass Department of Environmental Conservation

## Slide 2
Sub-standard
Culverts

## Slide 3: Glimpse of Existing Situation
A survey of 6,030 single and multiple culverts in five New England states:
 | Number | Percent
Severe barrier | 93 | 1.5
Significant barrier | 782 | 13.0
Moderate barrier | 2,347 | 38.9
Minor barrier | 2,539 | 42.1
Insignificant barrier | 269 | 4.5
Full passage | 0 | 0
53.4 % are moderate to severe barriers
None provided full aquatic organism passage

## Slide 4
Source: MA Riverways Program
721 sq.mi.

## Slide 5
Source: MA Riverways Program

## Slide 6
Source: MA Riverways Program

## Slide 7
Source: MA Riverways Program

## Slide 8
Source: MA Riverways Program

## Slide 9
MA River and Stream Crossing Standards
General Standards
  Open-bottom span preferred
  If culvert, then embedded:
    Min. 2ft (and at least 25% for round pipe culverts)
    Include substrate >15 inches in diameter, depths at least 2x D84 of embed material
  Min. 1.2x bankfull width
  Matches stream substrate
  Water depths & velocities that match natural stream at a variety of flows (low-flow channel)
  Openness: 0.82 ft. (0.25m)
  Banks on both sides of stream, match horizontal profile of existing stream and banks

## Slide 10
“No activity may substantially disrupt the necessary life cycle movements of those species of aquatic life indigenous to the waterbody, including those species that normally migrate through the area, unless the activity's primary purpose is to impound water. All permanent and temporary crossings of waterbodies shall be suitably culverted, bridged, or otherwise designed and constructed to maintain low flows to sustain the movement of those aquatic species.”
Nationwide Permit General Condition 2

## Slide 12: Evaluating Restoration Potential for Aquatic Barrier Removal
Habitat quality
  Occupancy
  Habitat suitability
  Habitat condition/ecological integrity
Enhanced connectivity
  Stream miles
  Connectivity metric

## Slide 13
Dams

## Slide 15: North Atlantic Aquatic Connectivity Collaborative (NAACC)

## Slide 16: North Atlantic Aquatic Connectivity Collaborative (NAACC): Objectives
Reconnect streams & rivers to support healthier populations of fish & wildlife
Proactively identify and prioritize sites for stream crossing upgrades/replacements
Facilitate communication and information sharing among partners

## Slide 17
Project Infrastructure
Crossing codes
Protocols & field data forms
Electronic data collection
Online Database
  Data storage & retrieval
  Scoring
  Mapping interface
Prioritizing crossings for assessment
Prioritizing crossings for mitigation
  TNC Northeast Connectivity Project
  UMass Critical Linkages Project

## Slide 19: NAACC Aquatic Connectivity Assessment

## Slide 20
Online Crossings Database

## Slide 21
Data Input
Paper forms
Electronic data collection
Bulk uploads

## Slide 22: Data Validation
Database rules that can’t be violated
Programmed in
Examples
  Required fields
  Acceptable range of measurements
  GPS units must be within bounding box
Electronic data collection: applied at time of collection in the field
Paper data collection: applied when data are entered to the database

## Slide 23: Scoring Systems
AOP Coarse Screen
Categorization
Limited number of variables used
3 Categories
  No AOP
  Reduced AOP
  Full AOP
Aquatic Passability Score
Numeric scoring
Based on a weighted combination of 14 variables
Scores range from
  0.0 (impassable) to
  1.0 (fully passable)

## Slide 24
Data from other Protocols
UMass: 11,626
Maine: 16,267
Vermont: 10,342
Connecticut: 2,493
NAACC (since 6/1/15)
32,040 records
102 Coordinators
568 Lead Observers

## Slide 25
TNC Northeast Aquatic Connectivity Project

## Slide 26
UMass Critical Linkages Assessment

## Slide 29
NAACC Culvert Condition Assessment

## Slide 30
Crossing Assessment Modules
Depth (detail)
Expert detailed assessment
Expert rapid
assessment
Lay person rapid assessment
Breadth (objective)
Aquatic
Connectivity
Geomorphic Vulnerability
Condition

## Slide 32
Percent increases in the amount of precipitation falling in very heavy events (defined as the heaviest 1% of all daily events) from 1958 to 2012 for each region of the continental United States
Source: updated from Karl et al. 2009
Notes: The map shows percent increases in the amount of precipitation falling in very heavy events (defined as the heaviest 1% of all daily events) from 1958 to 2012 for each region of the continental United States. These trends are larger than natural variations for the Northeast, Midwest, Puerto Rico, Southeast, Great Plains, and Alaska. The trends are not larger than natural variations for the Southwest, Hawai‘i, and the Northwest. The changes shown in this figure are calculated from the beginning and end points of the trends for 1958 to 2012. (Figure source: updated from Karl et al. 20091). (U.S. National Climate Assessment, 2014)

## Slide 34
Tropical Storm Irene

## Slide 35
Assessing vulnerability of road-stream crossings in the Deerfield River watershed

## Slide 36
Project Overview
How to assess and prioritize crossings for replacement
Deerfield River Watershed - road-stream crossings
Used existing methods to evaluate habitat fragmentation impacts
Developed new methods to assess vulnerability to extreme storm events under present and future climate conditions
Notes: Pilot study focused inland. Impt potential pts of failure for transp. Integrate multiple elts of vulnerability under current and predicted future climate conds

## Slide 37
Geomorphic
Ecological Disruption
Hydraulic
Criticality
Structural
Risk & Vulnerability
Project Components:
Transportation Vulnerability Ecological Vulnerability
Risk of Failure (road unusable)
  Structural (condition)
  Hydrologic/Hydraulic (flow, stream power)
  Geomorphic (river response – scour)
Criticality
  EMS Disruption
Ecological Disruption
  Impassability for aquatic species
  Aquatic connectivity restoration potential
  Coldwater streams
Notes: To come up with vulnerability score, looked at several risk factors. Potential disruption to Emergency Medical Services. Env services of structures if upgrade.

## Slide 39: Structural Risk of Failure
Based on:
  Rapid field assessment for culverts
  MassDOT bridge inspection reports
  Scored from 0 (low risk) to 1 (high risk)

## Slide 40: Geomorphic Risk of Failure
Failure mechanisms:
  Blockage by sediment
    Structure width/bankful width
    Specific stream power vs. bed resistance
    Observed erosion or aggradation
    Observed blockage
  Obstruction by woody debris
    Alignment
    Structure width
  Scour
    Specific stream power vs. bed resistance
    Sediment continuity
    Footing condition
    Downstream scour pool

## Slide 41: Hydraulic Risk of Failure
Hydrological models:
  Physical models
    HBV
    HSPF
    WRFH
  Statistical models
    Jacobs equation
    MA RPFE
Current vs Future:
  Mid-century
    9 climate models
  End-century
    Extrapolate from mid-century

## Slide 42
Current Hydraulic Risk Scores for each Hydrological Model

## Slide 43
Current and Mid Century Hydraulic Risk Scores for each Physical Model

## Slide 44
Hydraulic risk scores - current
Hydraulic risk scores – mid-century
Hydraulic risk scores – end-century

## Slide 45: Criticality: Disruption of Emergency Services
  Ambulance trips
  From depot to patient
  From patient to hospital
  Metrics
  Avg. delay
  Avg. affected delay
  Max. delay
  Integrated delay

## Slide 46: Overview of Approach
10
5
5
8
20
20
Incident 1

## Slide 47: Overview of Approach
10
5
5
8
20
20
20 minutes
Incident 1

## Slide 48: Overview of Approach
10
5
5
8
20
20
23 minutes
Delay: 3
Incident 1

## Slide 49: Overview of Approach
10
5
5
8
20
20
20 minutes
Incident 1

## Slide 50: Overview of Approach
10
5
5
8
20
20
40 minutes
Delay: 20
Incident 1

## Slide 51
3,144 real EMS calls
5,000 synthesized EMS calls

## Slide 53: Ecological Disruption
Based on:
  Aquatic Passability scores from NAACC
  Predicted temperature from Ecosheds.org
  UMass Critical Linkage analysis
  TNC aquatic barriers analysis
Metrics:
  Impassability (NAACC)
  Connectivity loss (Critical Linkages)
  Connectivity restoration potential (Critical Linkages)
  Anadromous restoration potential (TNC)
  Coldwater connectivity restoration potential (Critical Linkages)
    16 C, 18 C, 20 C, & 22 C
    Current & Future

## Slide 55
Stream Crossings Explorer sce.ecosheds.org

## Slide 56
Thank You

## Slide 58
Notes: First screen that appears, once you have seen the video and the tutorial and checked the default attributes

## Slide 59
Notes: Can filter on state, town, road jurisdiction, DOT district, HUC12 watershed, etc.

## Slide 60
Notes: With charts you add what attribute you want to filter on

## Slide 61
Notes: Here we choseOverall EMS Delay, and filtered on scores>0.8

## Slide 62
Notes: Click on an individual crossing and see all the feature attributes you chose to see, for that crossing.